8th lecture: Summary 7th lecture: NMR

Spin resonance:

linear rf-field:	  			   Rotating field approximation:

. .

In the rotating frame: effective field , i.e.:	.

At resonance : Rotating frame: M precesses about B1;

Lab. frame:       M spirals up and down:

NMR: , T = 300 K, B = 10 T.

1. Spin-lattice relaxation time T1: fluctuating  at ω0 establish energetic equilibrium of Mz (~ sec).

2. Spin-spin relaxation time T2 < T1: fluctuating Bz destroy , increase entropy: decoherence (~ msec),

lead to homogeneous broadening by spin flip-flop processes (Lorentzian),

and to inhomogeneous broadening by non-uniform B0(x): .

This is also described by Bloch equations:

and .

Solutions for Mz = M0:  and ,

with dispersive and resonant Lorentz curves: , .

In solids: static internal fields Bz from randomly orientated neighbor spins make additional Gaussian broadening.

In liquids: these Bz are averagen out due to motional narrowing.

Pulsed NMR: π/2-flip, spectrum from free induction decay:

Chemical shifts by chemical environment = finger-print of the molecule:

4.4 Some special NMR techniques

a) Spin-echo (SE)

- NMR-SE in sample

rf-pulse sequence:

leads to time sequence of magnetization (in rotating frame):

produces NMR signal:

After 'refocussing' 180o-flip:

| At a main field of 1.5 T |
| --- |
| Tissue Type | T1 in ms | T2 in ms |
| Adipose tissues | 240-250 | 60-80 |
| Whole blood (deoxygenated) | 1350 | 50 |
| Whole blood (oxygenated) | 1350 | 200 |
| Cerebrospinal fluid | 2200-2400 | 500-1400 |
| Gray matter of cerebrum | 920 | 100 |
| White matter of cerebrum | 780 | 90 |
| Liver | 490 | 40 |
| Kidneys | 650 | 60-75 |
| Muscles | 860-900 | 50 |

All coherence losses due to inhomogeneous B0-field cancel (T2inhom).

Main use of NMR-SE: measurement of T2:

2. Atomic or nuclear SE in-beam:

Like NMR-SE, but 'in-flight':

All coherence losses due to different times of flight (TOF) cancel, i.e. a 'white atomic beam' can be used.

Main use of ABSE: measurement of the sample's time-correlation function ,

with particle density ρ(t). G(t) gives the probability that the system changes within time t. Explanation:

1.	atoms' polarization is flipped by π/2, from Pz to , in low field.

2. 	The beam enters B0-field region: the longitudinal Stern-Gerlach effect

slows down the spin-up partial amplitude (relative to B0), accelerates the spin-down partial amplitude.

3.	spin-up and spin-down arrive on the sample with a time difference , called the spin echo time,

which is a property of the apparatus, as discussed on the next page.

- The value of maximum Pz at the spin-echo point equals  (without proof).

Measurements at different  gives the complete time-correlation function G(t), with .

When G(t) is measured under different scattering angles θ,

that is for different momentum transfers ħq to the sample: ,

one obtains G(q, t), i.e. one probes the system at different spatial scales .

The Fourier transform gives the sample's space-time correlation function .

Derivation of the SE time  from simple kinematics:

The TOF of the atom through the magnetic field region of length L is .

Without magnetic field, .

With magnetic field, due to the 'longitudinal Stern-Gerlach' effect,

the velocity changes, for the spin-up and down amplitudes, to

, for magnetic potential Emagn << Ekin.

With , the SE time becomes .

With , this becomes .

(BL usually must be replaced by the magnetic field integral along the flight path z).

Hence,  can be varied by varying the magnetic field B along the beam.

Measurement the SE signal for various magnetic fields B directly gives the time-correlation function G(t).

Neutron-SE:

Spin dynamics of mono-domain Fe particles in Al2O3, at q = 0.07Å-1.

The measurement at a correlation time of 200 ns in this experiment

is equivalent to a measurement at an energy transfer of about 10 neV.

b) Multidimensional NMR

The spin-echo principle can also be used to study the

interaction of one nucleus with its molecular neighbour nuclei.

One vayies the delay t1/2 between the first π/2 pulse

and the refocussing pulse, and measures the spin-echo signal

f(t1, t2) as a function of two time scales.

The signal then contains information to what extent

magnetization is transferred from one nucleus to its neighbors.

Double Fourier transformation then gives a two-dimensional spectrum g(ω1, ω2).

From the angular and distance information encoded in this spectrum one can

build up the whole 3-dimensional molecular structure.

Multidimensional NMR techniques currently allow		2-dim NMR spectrum of erythromycin in D2O.

structure determination of proteins up to 50 kDa.

c) Magnetic resonance imaging

B0- field along body axis z. Spatially resolved NMR-signal for position (x0, y0, z0) by:

z0:  Slice selection:

Strong static magnetic field gradient along axis z, selects slice through body at z0.

Apply π/2-pulse with the frequency ω0(z0) belonging to this slice.

Only nuclei in this slice will participate in the following operations.

x0: Phase encoding:

a small gradient of short duration is applied along x:

the precessing magnetization  gets a different phase φ(x) for each line of the image.

y0: Frequency encoding:

then for some time a gradient is applied along y:

precesses with a different frequency ω0(y) for each line of the image.

For a given z0, the x-y-resolved free induction signal is Fourier transformed to an image

whose intensity is modulated as a function of proton density, relaxation time T2, …

d) Ramsey's separated oscillatory field method

1. Rabi's method: Spin resonance in-flight

Polarized atomic beam in a magnetic field B0 transverses

oscillatory field region where a spin-flip is induced at frequency .

The spin-flip is detected in an analyzer/detector setup.

The minimum width of the resonance signal is given

by the TOF t through the resonance region: .

2. Ramsey's method: separated oscillatory fields

The TOF can be significantly increased by using two successive rf-field pulses,

separated either in space (for an atomic beam) or in time (for trapped atoms).

The two rf-fields come from the same oscillator,

so they are always in phase with each other.

First rf-pulse: induces a π/2-flip to the polarization: .

The transverse polarization  precesses about B0 during its TOF to the second rf-coil.

Second rf-pulse: induces a second π/2-flip , but only if

the atoms' transverse polarization has exactly the same phase as the rotating rf-field,

i.e. if it precesses, during its TOF, at the same frequency  as the rf-field.

By scanning B0 one obtains very narrow 'Ramsey-fringes' in the signal,

again convoluted with the atomic beam's TOF spectrum.

Applications:

1. Time/frequency standard in atomic clocks (in-beam):

Lock the external oscillator frequency to the Larmor frequency of the

atom's hyperfine transition, which then determines the length of a second.

2. Precision measurements on atomic transition under various conditions

(in-trap or in-beam)

Example: CP-violating electric dipole moment of the neutron (in n-bottle)

Neutron spin precession frequency in Hz

Double pulse NMR signal from 10,000 polarised neutrons

Neutron spin-precession frequency

Double-pulse signal from 10,000 polarized neutrons

stored in the apparatus for 150 s, which is used to search

for an electric dipole moment (EDM) to the neutron.

The double-pulse interference pattern is analogous to the

well known double-slit interference pattern in optics.

A shift in the interference pattern of one linewidth would correspond

to a magnetic field change of 10−10 Tesla, or an EDM of 10-22 e cm.

e) Adiabatic theorem

The adiabatic theorem of quantum mechanics:

1. Adiabatic evolution: A physical system remains in its instantaneous eigenstate

if a given perturbation is acting on it slowly enough, that is:

When the Hamiltonian H(t) of a system changes slowly enough in the course of time t,

then the system will remain in the corresponding eigenstate of the final Hamiltonian.

Example: particle polarization  adiabatically follows slowly changing magnetic field B,

when frequency Ω of the turning magnetic field << Larmor frequency ω0:

2. Non-adiabatic evolution: Rapidly changing conditions prevent the system from adapting

its configuration during the process, hence the probability density remains unchanged.

The system ends in a linear combination of states (with respect to the final Hamiltonian)

that sum to reproduce the initial probability density.

Example: particle polarization does not follow rapidly changing magnetic field.

Current-sheet neutron spin-flipper:

without current (only small holding field):	  with current: field changes sign within the thin current-sheet:

NMR-Adiabatic fast passage:

Slow adiabatic sweep through the resonance at ω0

(though fast with respect to transverse relaxation time T2).

Far off resonance ω << ω0, the magnetization M is 'upwards' along z.

When the frequency slowly approaches resonance,

Beff is changing its direction adiabatically towards x.

After the sweep, at ω >> ω0, the magnetization is 'downwards' opposite to z.

The method works both for a frequency sweep and a magnetic field sweep.

Example: rf-spin flipper in-beam:

adiabatic spin reversal during passage through a non-uniform field B(z),

with superimposed rf-field of constant frequency .

# Text boxes

x

4.

Ωt = π

t or z

z

Pz = +1      B(z)       B(0)	      Pz = +1

B1cosωt

B0     z

Beff

B0−ω/γ

M

x

B1

2B1cosωt = B1+(t)   +   B1−(t)

1.

←	             →

=                   +

y0					y

3.

Spin-rotation curve					          Spin-echo curve

rotating

frame: 		        lab-frame:

z = z0:

y

+B

M

2.

from Stern-Gerlach polarizer

x0

Hz   ω

Stern-Gerlach analyzer

Pz

Pz

Interferometric fringe pattern

for Ca atoms at 10 mK.

I > 0:             z

+B           −B'

Pz > 0	            z      Pz < 0

A		C		B

B0

f(t)	       F-T  →    	   g(ω)

t			   ω

I = 0:

z        z

n

Pz > 0	                  Pz > 0

z

q = k − k0

k0

θ

q/2      k

θ/2

−q

V(z) for spin-up

E

Ekin

Emagn

z

B

−B