## Slide 1: Expected TPC performance in 2018 pb-pb collisions at high rates
Kai Schweda, GSI Darmstadt, for the ALICE TPC group

## Slide 2: Executive Summary
Readout rate (central triggers) optimum of 375 s-1 at 6 kHz, 355 s-1 at 10.9 kHz interaction rate
Distortions in IROCs (cover electrode potential +180V)
Drf < 1.0 cm (1.4 cm) at 8 kHz (10.9 kHz) Pb-Pb interaction rate
Distortions in OROC C06 (two floating gating grid wires, DHV = -50 V)
Drf < 4 cm (8 cm) at 8 kHz (10.9 kHz) Pb-Pb interaction rate
Particle identification PID separation power decreases by 10% from 6 kHz to 8 kHz IR

## Slide 3: Readout rate
Multi event buffering (4x)
Maximum readout rate of 375 s-1 at 6 kHz
Decreases linearly to 355 s-1 at 10.9 kHz
Double rate compared to former RCU

## Slide 4: Distortions in inner rocs
Drf < 1.0 cm at 8 kHz can be well calibrated back to design performance
Drf < 1.4 cm at 10.9 kHz can be calibrated fluctuations might play a (small) role  time-dependent QA to filter out events with large fluctuations

## Slide 5: Distortions in outer roc c06
OROC C06 has two floating gating grid wires
anode voltage reduced DHV = -50 V
Drf = 4 cm at 8 kHz can be calibrated
Drf = 8 cm at 10.9 kHz  cluster loss fluctuations play a role
Also: OROC A05 at DHV = -60 V for operational stability

## Slide 6: Particle identification
p / e (LHC15o, Pb-Pb) dE/dx separation power decreases linearly with interaction rate (occupancy)
number of wrongly assigned clusters increases
Decrease is 10% from 6 kHz to 8 kHz